## Slide 1
Practical information about the vf2TDC
Document link
Overview of the board
Variations (current status)
Latest order

## Slide 2
1. Document link
/group/da/distribution/coda/HardwareManual/vfTDC/
  vfTDC.docx, vfTDC.pdf: vf2TDC user manual
  vfTDC.pptx: a short presentation about the vf2TDC, resolution etc.

## Slide 3
Practical information about the vf2TDC
Document link
Overview of the board
Variations (current status)
Latest order

## Slide 4
2. Overview of the board
The SET:
  VETROCbase, 6U VME64x, 64 differential channels plus 8 differential inputs and 8 ECL outputs
  2x VETROCmezz, 32-ch differential receiver (to LVTTL)
  VETROCio, 6U VME64x, P2 IO card, 64-ch differential receiver (to LVTTL)

## Slide 5
Trigger Interface (fiber)
Trg/Clk/Reset/Busy
4x Rx/Tx (QSFP)
VXS P0:
Trg/Clk/Reset/Busy (SD)
4x Rx/Tx (to SW#A)
32 LVTTL in
32 differential in
Generic
8 differential In
8 ECL out
32 LVTTL in (with mezz. for differential IN)
32 differential in
28 LVTTL on row A
4 + 4 LVTTL on row D
28 LVTTL on row C
2x Rx/Tx on row A & C
VME64x:
Register,
Data Readout
FPGA, XC7A200T-2FF1156C
18Mbit RAM
2. Overview of the board, details about the 6U VME base board

## Slide 6
3. Variations (firmware)
3.1: 192-ch version (hardware: the SET)
There is a 4 µs ring buffer for every channel waiting for the readout trigger’s arrival. The data buffer is implemented in FPGA’s BRAM (~100 Kbyte). This data buffer can be expanded to the external 2 Mbyte ram. The TDC resolution (rms) ~ 30 ps.
This firmware is used in HallA.
3.2: 64-ch version (hardware: The 6U vme base board only)
There is a 8 µs ring buffer for every channel waiting for the readout trigger’s arrival. The edges are measured (at least) twice for better timing resolution and large delay cell mitigation. The data buffer is implemented in FPGA’s BRAM (~100 Kbyte). This data buffer can be expanded to the external 2 Mbyte ram. The TDC resolution (rms) ~ 20 ps.
This firmware is used in HallB.

## Slide 7
4. Lastest order (the cost)
FY2024
  PCB orders: PR# 430581, 424127
  Front panels: PR#432423, 423948, I1, I2,
Costs:
  VETROCbase: ~$1700 each at the quantity of 60
  VETROCio: ~$450 each at the quantity of 40
  VETROCmezz: ~$110 each at the quantity of 80
  The 192-channel version: ~$2350 each
  The 64-channel version: ~$1700 each
    * But, (much) higher price for small quantity orders